## Slide 1
09 March 2012
<number>
Liquefaction
Elected Member Workshop
SmartGrowth,
TCC Chambers
10 April 2013
Lq. = Liquefaction effects ( inc. lateral spread)
Ls = lateral spread ground damage
Notes: <number>

## Slide 2: Liquefaction – The Basics What is liquefaction?
09 March 2012
<number>
Some soils, when located below the ground
water table, start acting like a liquid when
they are severely shaken or vibrated.

## Slide 3: Liquefaction – The Basics What has to be present?
09 March 2012
<number>
A granular soil with little or no clay material in it
The soil particles are mainly between 1/100 mm & 1 mm in size – “coarse silts” to “fine sands”
Soil is under water
Earthquake of large enough size
Shaken not Stirred! … liquefaction

## Slide 4
Non-liquefying Crust
Liquefying Soil
Crust thinning example
Original Ground Surface
Ground Water Level
Phase 1 – Ground Surface Settlement
Phase 2 – Structures Sink into the Ground (Bearing Capacity Failure)
Phase 3 – Soil Regains its Original Strength (Resolidification)
Notes: You will have heard about crust thinning and the subsequent reduction in capacity of land to support buildings and this explains how that works.
<number>

## Slide 5: TCC
09 March 2012
<number>
What have we been doing?
Notes: <number>

## Slide 6
09 March 2012
<number>
Received advice from Cat 1 geotechs – 1998 to 2002
GNS / Opus Microzoning Reports – 2003 and 2006
Compiled for Lifelines and planning purposes respectively – 500 & 2500yr return period e/quakes
Used historic geo & GCR reports; very limited testing; large scale geo maps
4 quake sources – risk map based on Tga Local source
Ground damage map for areas susceptible to Lq. – none, minor, limited, moderate, large, major, extensive
Effect - minor < 100mm & small lateral spread;
moderate 100mm – 300mm & < 50m significant Ls, 50 – 100m minor Ls;
extensive > 300mm & < 50m extensive Ls, 50 – 200m significant LS; balance areas – very extensive
Updated map compiled
Notes: <number>

## Slide 8: What have we been doing? cont’d
Geotech reporting – RC and s224 – short term
Reviewed technical info – early 2012
Reviewed statutory requirements – RMA / BA
3 Geo-professional workshop – agreed proposed development approach and assessment criteria – April 2012
2 Developer / Building Industry workshop – reviewed & approach agreed
2 Meet - Firth
RMA procedure – implemented – May 2012 (low compliance / development cost impact)

## Slide 9: Agreed Assessment Guideline
09 March 2012
<number>
Guideline published - NZ Geotech Society
Guidance on
  Site investigation, assessing, effects & remediation
  soils properties based on past practice / experience / testing.
Uses NZS 1170 to determine:
  ground acceleration (7.5 quake); &
  SLS (25 yr event, structure must be repairable) & ULS (500 yr event, structure not repairable but must not collapse)
Notes: <number>
Extent of investigation and testing – see 6.2.1 NZGS – investigation plan - #s of CPTs per site – devp vs. new dwelling?
Software packages
Plasticity limit testing and particle distribution testing.
Aspects of guidelines agree to use – parameters, approaches from various section – PGA values
Report on three aspects – see page 15 NZGS Guide
What is deemed significant/insignificant/excessive?
Retain SLS and ULS current practice and requirement? Use TC1 2 and 3 criteria for SLS and ULS design (table 3.1 DBH)?
Tauranga related design guidance document? Based on DBH?

## Slide 10: What’s next – TCC?
09 March 2012
<number>
Firth design solutions
Firth / geo-professional workshop – review foundation design solns.
Final internal review and sign off
Re-present to Developer / Building Industry
Set implementation date – educate
Implement BA procedure – mid / late 2013
Undertake additional research work – verify 2002 / 2006 maps
Notes: <number>

## Slide 11: SmartGrowth Review - Liquefaction
Existing liquefaction maps (2003 / 2006) – show similar soils profiles to existing developed areas
Likely ground conditions – sands, organic deposits, probable similar ground water levels – (Bell Road e.gs. - sand mining, RR application)

## Slide 12: SG Review & Liquefaction cont’d. Future Work
GNS Proposal – 3 fold
  Update regional Lq / Ls maps (1 – 3yr)
  Detailed Lq / Ls assessment for future urban
  Detailed Lq / Ls assessment for existing urban ( both 3 – 20yr)
Use 2002 / 2006 approach include Chch findings etc.
Agree with approach – review timing

## Slide 13
09 March 2012
<number>
Discussion / Questions
Notes: <number>